## Slide 1
KNOWLEDGE INSTITUTE OF TECHNOLOGY
PASSIVE COOLING
FOR HOME

## Slide 2
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Passive Cooling for Home
Objective: To reduce indoor temperature using only passive techniques — without mechanical or electrical cooling systems.
Solution: A semi-cylindrical dome-shaped prototype using natural ventilation, stack effect, Venturi effect, and solar-reflective materials.
Impact: Reduces indoor temperature by 2-3 degree C without energy consumption — sustainable, low-cost, and eco-friendly housing solution.
2

## Slide 3
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Engineering Design Process
1
Requirement Analysis:
Identified need for zero-energy cooling; studied climatic data of Salem, Tamil Nadu for solar radiation and wind patterns.
2
Architectural Design:
Designed semi-cylindrical dome (60x60 cm) with top air extractor, side window openings, and extended roof overhang.
3
Material Selection:
Selected cardboard and foam board for prototype; AAC blocks, Low-E glass, solar-reflective paint for full-scale.
4
Prototype & Testing:
Built cardboard dome; placed DS18B20 sensors to record indoor vs outdoor temperature with RTC and SD card logging.
3

## Slide 4
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Process Table
Phase
Activity
Outcome
Solar Heat Reduction
Reflective coating on dome exterior surface
Surface absorptivity reduced; less heat enters indoor space
Stack Effect
Warm air rises through dome apex top opening
Hot air exits naturally; cooler air drawn in from below
Venturi Effect
Air accelerates through constricted outlet openings
Air velocity increases; enhanced heat removal from interior
Cross Ventilation
Large side windows aligned with prevailing wind
Continuous fresh air flow across the occupied zone
Data Logging
DS18B20 sensors record T1 (outside) and T2 (inside)
Temperature data stored via RTC and SD card for analysis
4

## Slide 5
KNOWLEDGE INSTITUTE OF TECHNOLOGY
List of Activities
Field Visit: Visited a naturally cooled residential house near Dindigul to study passive design strategies and real construction techniques.
Prototype Fabrication: Built a 60x60 cm cardboard dome prototype with foam board insulation, top air extractor, and large side ventilation windows.
Sensor Integration: Installed DS18B20 sensors, RTC module, and SD card module to log indoor (T2) and outdoor (T1) temperatures continuously.
Testing and Analysis: Recorded temperature data under real outdoor conditions; analyzed T1 vs T2 difference to validate passive cooling performance.
5

## Slide 6
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Activity Duration Table
Activity ID
Task Description
Duration
A1
Field Visit and Climatic Data Collection (Salem, TN)
1 Week
A2
Architectural Design and Material Selection
1 Week
A3
Prototype Fabrication (Cardboard Dome Model)
2 Weeks
A4
Sensor Wiring and Data Logging Setup
1 Week
A5
Outdoor Testing, Data Recording and Analysis
3 Weeks
6

## Slide 7
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Activity Precedence Table
Activity
Preceded By
Logic
Prototype Fabrication
Field Visit and Design
Construction starts after site study and design finalization
Sensor Integration
Prototype Fabrication
Sensors mounted only after prototype structure is complete
Outdoor Testing
Sensor Integration
Testing starts once data logging system is fully operational
Data Analysis
Outdoor Testing
Temperature comparison done after sufficient data is collected
7

## Slide 8
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Glossary
Passive Cooling:
Cooling of indoor spaces using natural methods without any electrical or mechanical systems.
Stack Effect:
Natural air movement caused by temperature and density differences — warm air rises and exits at top.
Venturi Effect:
Air velocity increases when flowing through a constricted area, causing pressure drop and enhanced airflow.
AAC Blocks:
Autoclaved Aerated Concrete — lightweight, low-conductivity blocks used for thermal insulation in walls.
DS18B20:
High-accuracy digital temperature sensor (accuracy +/-0.5 degree C) for measuring indoor and outdoor temperatures.
Solar Reflective Paint:
Exterior coating that reflects infrared solar radiation, reducing surface temperature and heat gain.
8

## Slide 9
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Science Principles
Heat Transfer (Conduction, Convection, Radiation):
Low-conductivity materials reduce conduction; airflow drives convection; reflective coating cuts radiation heat gain.
Buoyancy (Stack Effect):
Warm air is less dense and rises to the dome apex, creating a pressure difference that draws cooler air from side openings.
Fluid Mechanics (Bernoulli Principle):
Pressure drops as air velocity increases at constricted outlet openings, pulling more air through the structure naturally.
Thermal Mass Effect:
AAC blocks and clay tiles absorb and delay heat, slowing the temperature rise inside the building during peak daytime.
9

## Slide 10
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Concept Rules and Laws
Solar Heat Gain Rule: Q_solar = alpha x I x A — reducing surface absorptivity directly reduces heat entering the building.
Continuity Equation: A1 x V1 = A2 x V2 — smaller outlet area increases air velocity, strengthening Venturi-driven ventilation.
Sensible Heat Removal: Q_air = m-dot x Cp x (Ti - To) — continuous air exchange removes accumulated indoor heat efficiently.
Thermal Resistance Rule: Higher R-value materials such as AAC and foam board slow down heat conduction through walls and roof.
Dome Geometry Principle: Corner-free curved surface distributes solar radiation uniformly and avoids localized heat accumulation zones.
10

## Slide 11
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Constants and Variables
CONSTANTS
Prototype Dimensions: 60 x 60 x 60 cm
Cardboard Conductivity: 0.05 to 0.10 W/m.K
Foam Board Conductivity: 0.03 to 0.05 W/m.K
DS18B20 Accuracy: +/- 0.5 degree C
Prototype Cost: Rs.1,420
Full-Scale Estimated Cost: Rs.56,000
VARIABLES
Indoor Temp (T2): Changes with design
Outdoor Temp (T1): Varies with time of day
Delta T = T1 - T2: Measures cooling effect
Air Velocity (v): Depends on wind and openings
Solar Intensity (I): Varies with season and time
11

## Slide 12
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Key Equations
System Logic Model
Solar Radiation >> Dome Roof >> Stack + Venturi Effect >> Natural Airflow >> Indoor Cooling
Solar Heat Gain: Q_solar = alpha x I x A (alpha = solar absorptivity; I = solar intensity W/m2; A = surface area m2)
Sensible Heat Removal: Q_air = m-dot x Cp x (Ti - To) (m-dot = mass flow rate; Cp = specific heat of air)
Continuity Equation (Venturi): A1 x V1 = A2 x V2 -- Smaller outlet = Higher air velocity
Result: Delta T = T1 - T2 = 2 to 3 degree C observed; confirms passive cooling effectiveness
12

## Slide 13
KNOWLEDGE INSTITUTE OF TECHNOLOGY
What-If Analysis
Q:
What if wind speed is very low?
-> Stack effect alone maintains airflow; dome top extractor continues to remove hot air via buoyancy forces.
Q:
What if solar radiation is very high?
-> Reflective coating reduces absorptivity; dome geometry distributes radiation uniformly, limiting peak heat gain.
Q:
What if materials change to concrete?
-> Higher conductivity increases heat gain; AAC blocks with Low-E glass must be used to maintain performance.
Q:
What if the top opening is blocked?
-> Hot air gets trapped; stack effect fails; indoor temperature rises — top extractor opening is critical to system.
13

## Slide 14
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Conclusion
Innovation:
Successfully built a zero-energy passive cooling prototype using dome geometry, stack effect, and Venturi-assisted airflow.
Efficiency:
Achieved 2-3 degree C indoor temperature reduction over outdoor without any mechanical or electrical cooling system.
Reliability:
DS18B20 sensor data confirmed consistent thermal performance; T2 remained stable even under increasing external conditions.
Future Scope:
Scale up with AAC blocks; integrate CFD simulation, IoT monitoring, wind catchers, and solar panel combination.
14